## Slide 1: MP/BME 710: Journal club
Magnetic Resonance Elastography of Liver:
Technique, Analysis, and Clinical Applications
Sudhakar K. Venkatesh, MD, Meng Yin, PhD, and Richard L. Ehman, MD
Grant Roberts
Department of Medical Physics

## Slide 2: Outline
Introduction
Liver Fibrosis
Basic Principles of MRE
MRE Sequence
Post-processing (Production of Elastograms)
Clinical Applications
Conclusion

## Slide 3: Introduction
Mechanical properties of tissues often change during disease
  Tumor (hard) vs. benign lipoma (soft)
  Muscle stiffness (muscular dystrophy)
  Viscoelasticity brain parenchyma
  Liver fibrosis
Palpation has been used for centuries
MRE allows quantitative analysis of mechanical properties
  “Virtual palpation”
Murphy MC, Jones DT, Jack CR, et al. Regional brain stiffness changes across the Alzheimer’s disease spectrum. NeuroImage Clin 2016;10:283–290.
Notes: Mechanical properties of tissues, specifically stiffness, provide valuable information about disease processes. For years, physicians have been using sense of touch (palpation) to aid in diagnosis by literally feeling the stiffness of organs, most markedly in differentiating malignant tumors (harder) and benign tumors (softer). However, there are other disease which change tissue stiffness that cannot be palpated non-invasively, such as stiffness of the brain in Alzheimer patients or liver fibrosis. MRE provides a way to non-invasively and quantitatively assess mechanical properties of tissues.

## Slide 4: Liver Fibrosis
Caused by various diseases
  Hepatitis A,B,C, alcoholism, portal vein thrombosis, NAFLD
Fibrosis is reversible at early stages
Diagnosing fibrosis
  Percutaneous biopsy (gold standard)
    Invasive, expensive, poor patient acceptance, risk of complication (~3%)
    Samples prone to inter-observer variability and poor repeatability
  Serum markers
    Variable accuracies
  Ultrasound Elastography (Fibroscan)
    Successful, but limited to localized spot measurements
    Obesity, ascites, bowel interposition may limit diagnostic accuracy
  MR Elastography
    Creates complete stiffness map of liver, more accurate than Fibroscan1
    Hepatic iron overload, breath-hold may limit diagnostic accuracy
https://www.youtube.com/watch?reload=9&v=TXxI4bB_CQY
1. Xiao H, Shi M, Xie Y, Chi X. Comparison of diagnostic accuracy of magnetic resonance elastography and Fibroscan for detecting liver fibrosis in chronic hepatitis B patients: A systematic review and meta-analysis. PLoS One 2017;12:1–14.
Notes: Liver fibrosis can be caused by a number of diseases, such as Hepatitis A,B,C, alcoholism, portal vein thrombosis, non-fatty liver disease, and many other diseases. If left untreated, this will eventually lead to non-reversible chirrosis. But, if detected early enough, can be reversible.

## Slide 5: Basic Principles of MRE
  Transverse waves are introduced by driver (20-200Hz)
    Active pneumatic driver placed outside of MR room
    Passive driver placed on patient
  Shear waves (longitudinal) are produced
  Wavelength dependent on shear modulus
    Waves propagate rapidly in stiff tissue, slower in softer tissue

## Slide 6: Basic Principles of MRE
Modified phase-contrast sequence
  Sensitized motion to cyclic displacement from shear waves
    Displacements on the order of microns
    Spins accumulate phase along bipolar or 1st order gradient
  Motion encoding gradients (MEG)
    Synchronized to driver frequency
    Can be placed in any dimension (x,y,z)
Venkatesh SK, Yin M, Ehman RL. Magnetic Resonance Elastography of Liver: Technique, Analysis, and Clinical Applications. 2013;37:544–555.

## Slide 7
Basic Liver Sequence
Short TR (50ms), short TE (20ms), and low flip angle (<30˚)
Requires less than a minute of acquisition time
  Uses fast sequences (EPI, GRE, or FSE)
  Only acquires 2-4 slices
Parallel imaging (x2)
256 x 64 matrix
Phase offsets = 4
Breath-hold (15 s)
Basic Principles of MRE

## Slide 8: Basic Principles of MRE

## Slide 9: Post-processing
How do we obtain pressure information from wave images?
Local frequency estimation
Inversion algorithm utilizing equations of motion to solve for shear modulus
  Without assumptions
    Inversion matrix = rank-4 tensor with 21 independent complex quantities
  Simplifying assumptions = incompressible, isotropic
    Inversion matrix reduced to 2 independent quantities
?

## Slide 10: Applying MRE to Liver
Normal liver parenchyma has shear stiffness < 3 kPa
Liver stiffness increases as histologic fibrosis increases
sfsf

## Slide 11: Clinical Applications

## Slide 12: Clinical Applications

## Slide 13: Conclusion
Benefits
Quick scan
Can be easily incorporated into liver protocols
  Dixon/IDEAL (measure fat)
  Diffusion Weighted (lesions, fibrosis)
  MRE (visualizing varices
  4D flow (flow in varices and portal hepatic system)
Reproducible across vendors and field strengths
Downsides
Lower resolution
Require breath-hold

## Slide 14: References
Venkatesh SK, Yin M, Ehman RL. Magnetic Resonance Elastography of Liver: Technique, Analysis, and Clinical Applications. 2013;37:544–555
Xiao H, Shi M, Xie Y, Chi X. Comparison of diagnostic accuracy of magnetic resonance elastography and Fibroscan for detecting liver fibrosis in chronic hepatitis B patients: A systematic review and meta-analysis. PLoS One 2017;12:1–14.
Murphy MC, Jones DT, Jack CR, et al. Regional brain stiffness changes across the Alzheimer’s disease spectrum. NeuroImage Clin 2016;10:283–290.

## Slide 15: Questions
Questions?